## Slide 1
Chapter 3
The Data Link Layer

## Slide 2: Questions for you
Why is Cellular Network called cellular?
Major differences among 1G, 2G, 3G, 4G, 5G
How satellite transmits data?

## Slide 3: Data Link Layer Design Issues (1 of 2)
Network layer services
Framing
Error control
Flow control

## Slide 4: Data Link Later Functions
Providing a well-defined service interface to the network layer.
Framing sequences of bytes as self-contained segments.
Detecting and correcting transmission errors.
Regulating the flow of data so that slow receivers are not swamped by fast senders.

## Slide 5: Data Link Layer Design Issues (2 of 2)
Relationship between packets and frames

## Slide 6: Services Provided to The Network Layer (1 of 2)
(a) Virtual communication. (b) Actual communication.

## Slide 7: Services Provided to The Network Layer (2 of 2)
Actual services vary from protocol to protocol
Three possible services
  Unacknowledged connectionless service
  Acknowledged connectionless service
  Acknowledged connection-oriented service

## Slide 8: Framing (1 of 4)
Framing methods
  Byte count
  Flag bytes with byte stuffing
  Flag bits with bit stuffing
  Physical layer coding violations

## Slide 9: Framing (2 of 4)
A byte stream. (a) Without errors. (b) With one error.

## Slide 10: Framing (3 of 4)
(a) A frame delimited by flag bytes. (b) Four examples of byte sequences before and after byte stuffing.

## Slide 11: Framing (4 of 4)
Bit stuffing. (a) The original data. (b) The data as they appear on the line. (c) The data as they are stored in the receiver’s memory after destuffing.

## Slide 12: Error Control
Ensuring all frames are eventually delivered:
  To the network layer at the destination
  In the proper order
Ensures reliable, connection-oriented service
Requires acknowledgement frames and timers

## Slide 13: Flow Control
Controlling the sending of transmission frames at a faster pace than they can be accepted
Feedback-based flow control
  Receiver sends back information to the sender giving it permission to send more data
  Or receiver tells the sender how the receiver is doing
Rate-based flow control
  Protocol has a built-in mechanism
  Mechanism limits the rate at which senders may transmit data
  No feedback from the receiver is necessary

## Slide 14: Error Detection and Correction
Error-correcting codes
  Referred to as FEC (Forward Error Correction)
  Include enough redundant information to enable the receiver to deduce what the transmitted data must have been
Error-detecting codes
  Include only enough redundancy to allow the receiver to deduce that an error has occurred (but not which error) and have it request a retransmission
Key consideration is the type of errors likely to occur

## Slide 15: Error-Correcting Codes (1 of 4)
Hamming codes
Binary convolutional codes
Reed-Solomon codes
Low-Density Parity Check codes

## Slide 16: Error-Correcting Codes (2 of 4)
Example of an (11, 7) Hamming code correcting a single-bit error

## Slide 17: Error-Correcting Codes (3 of 4)
The NASA binary convolutional code used in 802.11
The encoder has memory!

## Slide 18: Error-Correcting Codes (4 of 4)
Reed-Solomon codes
  Linear block codes
  Often systematic
  Codes are based on the fact that every n degree polynomial is uniquely determined by n + 1 points
LDPC (Low-Density Parity Check) codes
  Linear block codes
  Each output bit is formed from only a fraction of the input bits
  Practical for large block sizes
  Have excellent error-correction abilities that outperform many other codes

## Slide 19: Error-Detecting Codes (1 of 3)
Linear, systematic block codes
  Parity
  Checksums
  Cyclic Redundancy Checks (CRCs)

## Slide 20: Error-Detecting Codes (2 of 3)
Interleaving of parity bits to detect a burst error

## Slide 21: Error-Detecting Codes (3 of 3)
The word “checksum” is often used to mean a group of check bits associated with a message, regardless of how the bits are calculated.
A group of parity bits is one example of a checksum.
Stronger checksums based on a running sum of the data bits of the message.
The checksum is usually placed at the end of the message, as the complement of the sum function.

## Slide 22: Error-Detecting Codes (3 of 3)
Example calculation of the CRC
A third and stronger kind of error-detecting code is in widespread use at the link layer: the CRC (Cyclic Redundancy Check), also known as a polynomial code.
Polynomial codes are based upon treating bit strings as representations of polynomials with coefficients of 0 and 1 only.

## Slide 23: Elementary Data Link Protocols
Assumptions underly the communication model
Three simplex link-layer protocols
  Utopia: No Flow Control or Error Correction
  Adding Flow Control: Stop-and-Wait
  Adding Error Correction: Sequence Numbers and ARQ

## Slide 24: Initial Simplifying Assumptions (1 of 2)
Independent processes
  Physical, data link, and network layers are independent
  Communicate by passing messages back and forth
Unidirectional communication
  Machines use a reliable, connection-oriented service
Reliable machines and processes
  Machines do not crash

## Slide 25: Initial Simplifying Assumptions (2 of 2)
Implementation of the physical, data link, and network layers

## Slide 26: Basic Transmission And Receipt (1 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 27: Basic Transmission And Receipt (2 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 28: Basic Transmission And Receipt (3 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 29: Basic Transmission And Receipt (4 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 30: Basic Transmission And Receipt (5 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 31: Basic Transmission And Receipt (6 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h (end of code)

## Slide 32: Simplex Link-Layer Protocols (1 of 10)
Utopia: No Flow Control or Error Correction
Adding Flow Control: Stop-and-Wait
Adding Error Correction: Sequence Numbers and ARQ

## Slide 33: Simplex Link-Layer Protocols (2 of 10)
A utopian simplex protocol … continued on the next slide

## Slide 34: Simplex Link-Layer Protocols (3 of 10)
A utopian simplex protocol … continued on the next slide

## Slide 35: Simplex Link-Layer Protocols (4 of 10)
A utopian simplex protocol (end of code)

## Slide 36: Simplex Link-Layer Protocols (5 of 10)
A simplex stop-and-wait protocol … continued on the next slide

## Slide 37: Simplex Link-Layer Protocols (6 of 10)
A simplex stop-and-wait protocol … continued on the next slide

## Slide 38: Simplex Link-Layer Protocols (7 of 10)
A simplex stop-and-wait protocol (end of code)

## Slide 39: Simplex Link-Layer Protocols (8 of 10)
A positive acknowledgement with retransmission protocol … continued on the next slide

## Slide 40: Simplex Link-Layer Protocols (9 of 10)
A positive acknowledgement with retransmission protocol … continued on the next slide

## Slide 41: Simplex Link-Layer Protocols (10 of 10)
A positive acknowledgement with retransmission protocol (end of code)

## Slide 42: Improving Efficiency
Need bidirectional data transmission
Link layer efficiency improvement
  Send multiple frames simultaneously before receiving an acknowledgement

## Slide 43: Bidirectional Transmission, Multiple Frames in Flight (1 of 3)
Bidirectional transmission: piggybacking
  Use the same link for data in both directions
  Interleave data and control frames on the same link
  Temporarily delay outgoing acknowledgements so they can be hooked onto the next outgoing data frame
Piggybacking advantages
  A better use of the available channel bandwidth
  Lighter processing load at the receiver
Piggybacking issue
  Determining time data link layer waits for a packet to piggyback the acknowledgement

## Slide 44: Bidirectional Transmission, Multiple Frames in Flight (2 of 3)
Three bidirectional sliding window protocols
  One-bit sliding window, go-back-n, selective repeat
Consider any instant of time
  Sender maintains a set of sequence numbers corresponding to frames it is permitted to send
  Frames are said to fall within the sending window
  Receiver maintains a receiving window corresponding to the set of frames it is permitted to accept
Differ among themselves in terms of efficiency, complexity, and buffer requirements

## Slide 45: Bidirectional Transmission, Multiple Frames in Flight (3 of 3)
A sliding window of size 1, with a 3-bit sequence number. (a) Initially. (b) After the first frame has been sent. (c) After the first frame has been received. (d) After the first acknowledgement has been received.

## Slide 46: Examples (1 of 20)
A 1-bit sliding window protocol … continued on the next slide

## Slide 47: Examples (2 of 20)
A 1-bit sliding window protocol … continued on the next slide

## Slide 48: Examples (3 of 20)
A 1-bit sliding window protocol (end of code)

## Slide 49: Examples (4 of 20)
Two scenarios for protocol 4. (a) Normal case. (b) Abnormal case. The notation is (seq, ack, packet number). An asterisk indicates where a network layer accepts a packet.

## Slide 50: Examples (5 of 20)
Pipelining and error recovery. Effect of an error when (a) receiver’s window size is 1 and (b) receiver’s window size is large.

## Slide 51: Examples (6 of 20)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 52: Examples (7 of 20)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 53: Examples (8 of 20)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 54: Examples (9 of 20)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 55: Examples (10 of 20)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 56: Examples (11 of 20)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 57: Examples (12 of 20)
A sliding window protocol using go-back-n (end of code)

## Slide 58: Examples (13 of 20)
Simulation of multiple timers in software. (a) The queued timeouts. (b) The situation after the first timeout has expired.

## Slide 59: Examples (14 of 20)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 60: Examples (15 of 20)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 61: Examples (16 of 20)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 62: Examples (17 of 20)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 63: Examples (18 of 20)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 64: Examples (19 of 20)
A sliding window protocol using selective repeat (end of code)

## Slide 65: Examples (20 of 20)
(a) Initial situation with a window of size 7. (b) After 7 frames have been sent and received but not acknowledged. (c) Initial situation with a window size of 4. (d) After 4 frames have been sent and received but not acknowledged.

## Slide 66: Data Link Protocols in Practice
Packet over SONET
ADSL (Asymmetric Digital Subscriber Loop)

## Slide 67: Packet over SONET (1 of 4)
Packet over SONET. (a) A protocol stack. (b) Frame relationships.

## Slide 68: Packet over SONET (2 of 4)
PPP (Point-to-Point Protocol) features
  Separate packets, error detection
  Link Control Protocol (LCP)
  Network Control Protocol (NCP)

## Slide 69: Packet over SONET (3 of 4)
The PPP full frame format for unnumbered mode operation

## Slide 70: Packet over SONET (4 of 4)
State diagram for bringing a PPP link up and down

## Slide 71: ADSL (1 of 2)
ADSL protocol stacks

## Slide 72: ADSL (2 of 2)
AAL5 frame carrying PPP data

## Slide 73: Data Over Cable Service Interface Specification (DOCSIS)
DOCSIS Frame to codeword mapping

## Slide 74: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.